Lesson 42 Worksheet
1. vcold = 320 m/s
   vwarm = 384 m/s

   (ie. Sound travels faster in warm air, slower in cold according to:
   vsound = 331.4 + (0.69T)
   Where T is the temperature.)

   Given: Angle of incidence = 30 degrees.

   Given: Wavefront is nearly linear means that the incident sound wave travels in a near straight line. This is an ideal condition since physical factors such as non-uniformm air temperature can vary on the wavefront.

   n = sin i / sin R
   n = vi/vf

   {sin {%THETA%} sub i} over {sin {%THETA%} sub R} = {v sub i} over {v sub f}

   Solve for R.

   R = sin-1({(sin i)(v2)} over v1)
2. The radio will respond to the direct singal from the transmitter and to the reflected signal. If the two signals received by the radio are in one phase, constructive interference will occur and the radio will produce a sound. If the two signals are out of phase, destructive interference will occur and the radio will not play Justin Beiber. (Yay!)

   When the girl moves from a distance of 9.0 m, the intensity of the signal goes from a max to a min.

   1 over 2 {%lambda%} = 18